## Slide 1
ELI Summer School 2019
Dolní Břežany, Czech Republic
August 28th, 2019
MAC
Scientific end station
for gas phase targets
at the ELI Beamlines
HHG source
Maria Krikunova

## Slide 2
MAC user end-station
MAC - Multi-purpose user end-station
for AMO (atomic, molecular and optical) sciences and CDI coherent diffractive imaging
Main purpose:
Time-resolved experiments with coincident electron/ion spectroscopy and coherent diffractive imaging
to study structure and dynamics of matter
28.08.2019
2
Atomic and molecular systems under intense X-ray radiation,
M. Krikunova, N. Timneanu, J. Andreasson,
ISBN 978-3-319-20172-6

## Slide 3
Amazing combination
of VUV/XUV with optical pulses
Femtochemistry –Molecular reactions on a fs time-scale
M. Krikunova et al, J. Chem. Phys. 134 (2011) 024313
M. Krikunova et al, Phys. Rev. A 86 (2012) 043430
Time resolved ion spectroscopy on molecular iodine - different reactions channels are studied within one experimental run
Experiment at Free Electron Laser in Hamburg –
FLASH
3
28.08.2019

## Slide 4
Amazing combination
of VUV/XUV with THz pulses
Time of the electron birth
T. Oelze et al, Sci. Rep. 7 (2017) 40736
T. Oelze et al, Phys. Rev. A 99 (2019) 043423
THz field streaking is sensitive
to the electron birth time
Experiment at FLASH
4
28.08.2019

## Slide 5
Unique combination of spectroscopy with imaging
Ultrafast dynamics within a single shot
D. Rupp et al, Phys. Rev. Lett. 117 (2016) 153401
L. Flückiger et al, New J. Phys. 18 (2016) 043017
Experiment at FLASH
Experiment on single nanoparticles –
possibility to sort experimental data according to irradiation intensity as well as nanoparticle size
5
28.08.2019

## Slide 6
MAC user end-station
Spectrometers:
Time-of-flight electron / ion spectrometers
Velocity Map Imaging (VMI)
Magnetic bottle (under development)
Imaging XUV detectors:
PI-MTE in vacuum for 1eV to 10 keV photons
13.5 x 13.5 m pixel size
Andor I-Kon flange-mounted for VUV spectroscopy
13.5 x 13.5 m pixel size
CCD with phosphor screen
Sample delivery systems:
Cluster source based on cryo-cooled Even-Lavie-Valve
Microfluidic gas-dynamic nozzle
Aerosol nano-particle injector
Pump beams:
OPA beam 240 – 2600 nm
Few-cycle beam from hollow fiber compressor
Multi-cycle tunable THz source 4-18 THz
Single-cycle broadband ~1THz source
6
28.08.2019

## Slide 7
This work has been supported by the project
Structural dynamics of biomolecular systems (No. CZ.02.1.01/0.0/0.0/15_003/0000447) from European Regional Development Fund
and by the project Advanced research using high intensity laser produced photons and particles
(No. CZ.02.1.01/0.0/0.0/16_019/0000789) from European Regional Development Fund.
MAC team
Maria Krikunova: Team leader
Eva Klimesova: PostDoc
Andreas Hult Ross: PostDoc (started in July 2019)
Ziaul Md Hoque: PostDoc (supporting the MAC team)
Open position – PostDoc or PhD
Former team members:
Laura Dittrich: M. Sc. Student (finished in July 2018)
Olena Kulyk: PostDoc (finished in June 2019)
7
28.08.2019

## Slide 8
MAC user end-station
E1 experimental hall in January 2019
HHG
28.08.2019
8

## Slide 9
V. E. Nefedova et al., Phys. Rev. A 98 033414 (2018)
HHG - High Harmonic Generation
I.V. Hertel and C.-P.Schulz. Atome, Moleküle und optische Physik 1, Springer-Verlag Berlin, Heidelberg, 2008
Monochromator -
to select individual harmonics
28.08.2019
9

## Slide 10
Pulse-front tilt
Example: 5-mm FWHM beam, =30 nm (41 eV), 300 gr/mm grating, normal incidence
 1500 illuminated grooves
 path-difference OPFWHM = 45 m, tFWHM = 150 fs
Collaboration with Luca Poletto National Research Council
Institute of Photonics and Nanotechnologies
Padova, Italy
The trick to preserve the temporal duration of the XUV pulse is to keep the number of illuminated grooves as close as possible to the resolution /D
Monochromator –
to select individual harmonics
Pulse front tilt due to the angular dispersion
28.08.2019
10

## Slide 11
Time preserving monochromator –
to select individual harmonics
W. Cash, Appl. Opt. 21 710 (1982)
W. Werner & H. Wisser, Appl. Opt. 20 487 (1981)
W. Werner and H. Visser, Appl. Opt. 20, 487 (1981)
OFF-PLANE MOUNT  the incident and diffracted wave vectors are almost parallel to the grooves
28.08.2019
11

## Slide 12
Time preserving monochromator –
to select individual harmonics
Energy resolution
Pulse duration
Calculated for 100 m slit and assuming 1 mrad full divergence
O. Hort et al, Opt. Express 27 351945 (2019)
28.08.2019
12

## Slide 13
MAC user end-station -
Pump-probe configurations in E1
HHG focusing with multilayer coated off-axis parabola
f=270 mm, angle 21.06°
Current configuration under commissioning -
HHG focusing with ellipsoidal mirror
13
Ellipsoidal | Imaging ratio 1:4.8
Entrance arm | 2400 mm
Exit arm | 500 mm
Incidence angle | 85°
Clear aperture | 90 mm x 15 mm
28.08.2019

## Slide 14
MAC user end-station -
ion and electron spectrometers
VMI – Velocity Map Imaging according to the design of Eppink and Parker
A.T.J. Eppink and Parker, Rev. Sci. Instrum. 68 3477 (1997)
Produced by
O+ ion image
28.08.2019
14

## Slide 15
Chamber was backfilled with Ar gas. Monochromatized HHG beam with grating G158 in 0th order (~25 - 40 eV estimated, due to the reflection efficiency of the grating)
MAC user end-station -
Results from the VMI commissioning in July 2019
Electron image
in velocity mapping mode
Ion image
in velocity mapping mode
Electron image
Spatial resolution mode
Together with our friendly users
Russell Minns and Joanne Woodhouse from University of Southampton, UK
James Thomson and Katharine Reid
from University of Nottingham, UK
28.08.2019
15
Running user program
Molecular Frame Photoelectron Angular Distribution as a Probe of Dynamic Structure

## Slide 16
Collaboration with Prof Raimund Feifel, Goteborg Univ., Sweden
Best detection range 0…300 eV, possible tuning to higher energy
2 m flight tube for long arm
Electron mode for long arm or 3 electrode lens for ion high resolution ToF mode
Short arm for ion measurement in coincidence with electrons in long arm
MAC user end-station -
Magnetic bottle electron/ion time-of-flight spectrometer
Initial design for coincident electron and ion coincident mode
28.08.2019
16

## Slide 17
MAC user end-station -
Magnetic bottle working principle
from S.Number et al, AIP Advances 5 117101 (2015)
Schematic diagram showing the helical motion of an electron moving in a magnetic filed
P. Kruit and F.H. Read, J. Phys. E: Rev. Sci. Instrum. 16 313 (1983)
28.08.2019
17

## Slide 18
MAC user end-station -
sample delivery systems
Cluster and cold molecular beam source
Adiabatic expansion of rare gases /
molecules
Cluster - size is tuned by temperature and pressure behind the nozzle
Even-Lavie Valve
Cryogenic, temperature controlled pulsed valve
for cryogenic supersonic expansion and Helium droplets experiments
under commissioning
28.08.2019
18

## Slide 19
MAC user end-station -
sample delivery systems
Cluster and cold molecular beam source
Adiabatic expansion of rare gases / molecules
Cluster - size is tuned by temperature and pressure behind the nozzle
Gas dynamic virtual nozzle to produce microscopic droplet streams
Aerodynamic lens stack to guide and focus nanoparticle beam in vacuum
Aerosol injector
19
28.08.2019
developed in group of Prof. Janos Hajdu at Uppsala University, Sweden

## Slide 20
20
MAC user end-station -
sample delivery systems
The „Uppsala“ injector based on
GVDN (gas dynamic virtual nozzle) and ALS (aerodynamic lens stack)
28.08.2019

## Slide 21
MAC user end-station -
sample delivery systems
The „Uppsala“ injector based on
GVDN (gas dynamic virtual nozzle) and ALS (aerodynamic lens stack)
Liquid
Gas
Aerosol
GDVN nozzle
ALS
28.08.2019
21

## Slide 22
MAC user end-station -
Commissioning experiments in S1
From first commissioning experiments
to the development of in-house research program
28.08.2019
22
E. Klimešova et al, Sci. Rep. 9 8851 (2019)
NIR laser: 800 nm, 120 fs, 1016 W cm-2
Ar or He gas through injector
CsCl salt nanoparticles
With increasing gas density / irradiation intensity ion peaks become broadened towards shorter TOFs – higher ion kinetic energies

## Slide 23
23
Plasma channel formation
in the carrier gas
PIC simulation + analytical calculation
PIC simulation – collaboration with RP6, Yanjun Gu
Plasma channel is formed
Coulomb explosion of positively charged channel
Investigation of carrier gas dynamics
Can be used to estimate gas density
Opens new possibilities to study dynamics in inhomogeneous samples
Or differential pumping might be needed to decrease gas density
E. Klimešova et al, Sci. Rep. 9 8851 (2019)
28.08.2019

## Slide 24
CsCl nanoparticles in strong NIR fields – ion hits and misses
24
All shots are the same
H+, He+ and H2O+ ions
He+ accelerated to 80 eV
New peaks: Cs+, Cl+, photons
H2O+ peak disappears
Cl+ is accelerated to 100 – 700 eV
He+ is accelerated to ~ 1 keV
H+ is accelerated to 100 – 200 eV
Single shot hits
Single shot misses
28.08.2019
prepared by E. Klimešova

## Slide 25
CsCl nanoparticles in strong NIR fields – electrons
Misses
Only broad electron signal
Energies up to 200 eV
25
Hits
Same broad electron signal as for misses
Photon peak appears
New: fast signal at 3 – 20 ns,
corresponding energies: 1 – 55 keV
28.08.2019
prepared by E. Klimešova

## Slide 26
MAC user end-station -
Experiments with aerosol nanoparticle injector
M. F. Ciappina et al,
Laser Phys. Lett. 10 (2013) 105302
M.H. Cho et al, Sci. Rep. 8 16924 (2018)
28.08.2019
26
Electron emission in the plasonic
enhanced near-field
ATI (above threshold ionization) at ~1013 W/cm2
Laser wakefield acceleration regime
Nanoparticle inserted into a plasma medium
Controllable and localized electron injection by the nanoparticles
0.5 PW Laser
Electron beam with a narrow energy spread

## Slide 27
We are looking forward to
fruitful collaborations and successful user experiments !